## Slide 1
Hands-On Workshop :
Embedded Systems with MATLAB
Presented by:
Ascendas Systems Thailand Ltd
Pattarapol S.
Application Engineering

## Slide 2: Prerequisite
Install MATLAB 2025b
Check ver –support
  MATLAB
  Simulink
  MATLAB coder
  Simulink coder
  Embedded coder
  Arduino Hardware support package
Wiring diagram
[Suggestion] MATLAB Onramp + Simulink Onramp

## Slide 3: Prerequisite Install “Simulink Support Package for Arduino Hardware”
    Go to Add Ons
    Searching for “Simulink Support Package for Arduino Hardware”

## Slide 4: Prerequisite Install “Simulink Support Package for Arduino Hardware”
    Go to “Install” and Click “Install”
    Confirm Selection  Wait until the installation process finished

## Slide 5: Prerequisite Install “Simulink Support Package for Arduino Hardware”
    After installation complete  Click “Setup now”
    Select hardware option  Click “Next”

## Slide 6: Prerequisite Install “Simulink Support Package for Arduino Hardware”
    Software may ask you if you want to install “PixyMon V2” *Skipped by Click Next*
    Connect your Arduino to your laptop  Confirm the COM port

## Slide 7: Prerequisite Install “Simulink Support Package for Arduino Hardware”
    Select “Verify the setup”  Click “Next” and “Test Connection”
    Click “Finish”  Hardware setup completed

## Slide 8: Prerequisite Wiring Diagram
12V Line |  | 
12 V+ [Adaptor] | --> | 12 V+ [L298N]
12 V- [Adaptor] | --> | 12 V- [L298N]
GND [Arduino] | --> | 12 V- [L298N]
5V Line |  | 
5V [Arduino] | --> | 5V [Encoder]
5V [Arduino] | --> | 5V [L298N]
GND [Arduino] | --> | GND [Encoder]
12V Motor |  | 
M+ [Motor] | --> | OUT3 [L298N]
M- [Motor] | --> | OUT4 [L298N]
Motor control |  | 
D3 [Arduino] | --> | IN3 [L298N]
D4 [Arduino] | --> | IN4 [L298N]
D9 [Arduino] | --> | ENB [L298N]
Encoder |  | 
D2 [Arduino] | --> | OUT [Encoder]